INTERNATIONAL DRAGON CLASS

BUILDERS RESPONSIBILITIES

GUIDANCE NOTES FOR NEW BUILDERS

# Class Rules

Builders Responsibilities are defined in the Class Rules, as are the specific measurement requirements for the construction of a finished boat, its spars and sails.

Rule 2.101 and 2.102  define the builders responsibilities, the access he should permit to Measurers during the building process and the material samples that must be provided to the IDA and ISAF

The process of setting up as a builder of Dragons is as follows.

1.A licence to build one boat may be obtained by application to ISAF and after approval of the Builders National Authority and the IDA.

2.If a licence is agreed by ISAF an ISAF sticker for each boat to be built is issued on receipt from the builder of the International Class Fee

3.The Chief Measurer or International Dragon Measurer should be consulted by the Builder to inspect his plans and compare them to Class Plans and Rules and advise on potential infringements. Any departure from these plans will require the approval of the Technical Committee.  The relationship between the Builder and the Chief Measurer is essential at this early stage to avoid misunderstandings and difficulties when the first and subsequent boats are measured.

4.The Measurer will advise on permitted materials and the necessity to achieve consistency  during construction. He will also advise on the Measurement Form and those sections of it which may cause difficulty to the Builder

5.The Measurer should be present at the weighing of the component parts individually before assembly. He should also advise on the rules regarding ‘bonding’ of these parts

6.At the measurement of the completed boat he will establish the correct stations, weigh the assembled boat, position the templates and measure the hull against them, carry out a swing test and if necessary drill the hull to establish uniform thickness of hull and deck throughout their length.

7.These consultations may require several visits during the building process and will be at the Builders expense.

8.In addition the builder must provide current ISAF approved templates (ordered through the IDA)  and arrange to have approved Swing Gear available  for the Swing Test, again these items are at the Builders expense.

9. Class Rule 2.102 requires that three samples  of not less than 0.0625 sq/m of hull and deck and a specification are provided to the IDA for checking that they comply with current Class Rules.

10. Class Rule 2.101 says that the licensed builder is solely responsible for ensuring that the class rules are complied with, and also says that the measurer shall be permitted to inspect the work at any time during it’s progress.

11. Class Rule 1.85 says that a copy of the completed and signed Measurement Form shall be supplied to the IDA Secretary by the builder.

12. If , after having had the first boat measured, a builder wishes to continue production he shall obtain from ISAF a full licence to do so. His application must be endorsed by the IDA and his National Yachting Authority.

David Dale

Secretary, IDA

12 July, 2005