Tohatsu Outboard Propeller Chart Propellers have two basic dimensions; diameter & pitch. Diameter is the distance measured across the propeller hub line from the outer edge of the circle that is made by the propeller's blades during rotation. Pitch is the distance that a boat will travel if rotated one revolution without any slippage. When describing a propeller both the diameter and pitch are given. The diameter is referenced first and the pitch is second. Therefore, a 12" x 9" propeller would have a 12-inch diameter and a 9-inch blade pitch. Theoretically, a propeller with a 14-inch pitch, when rotated one full turn, would advance a boat 14 inches through the water. In reality, no 14-inch pitch blade will advance a boat 14 inches with one full turn. This variance is referred to as slippage. In general, changing to a higher pitch prop will increase your top-end speed but reduce your acceleration (reduce your "hole-shot" power). On the other hand, decreasing the pitch will increase your hole-shot but sacrifice some of your top-end speed. If the hole-shot speed is important to you, for example if you pull water skiers most of the time, then you would want to go with a lower pitch prop and sacrifice some of your top-end speed but increase your hole-shot speed to get the skiers up faster. UNDER NO CIRCUMSTANCES SHOULD YOU EVER USE A PROP WHICH WILL ALLOW YOUR OUTBOARD TO OPERATE ABOVE THE OUTBOARD'S RECOMMENDED MAXIMUM RPM's! The propeller selection chart can be used to help you in selecting the correct propeller for your Tohatsu outboard. Remember that in any application, discrepancies in performance can result due to the different boat hull designs, the final carrying load and your particular needs. NOTE: It is highly recommended that the outboard be checked with a tachometer to ensure that the engine is operating within the correct MAXIMUM RPM RANGE. Models Load* Dia Pitch # Blades Standard Equipment Tohatsu Part # MFS2A & MFS3.5A (4-Stroke) Light 7.4 7 3  3F0641010M Moderate to Heavy 7.4 5.7 3 309641060M Heavy 7.4 4.5 3 314641030M M2.5A & M3.5A (2-Stroke) Light 7.4 7 3 3F0641010M Moderate to Heavy 7.4 5.7 3  309641060M Heavy 7.4 4.5 3 (recommended for 2.5 only) 314641030M M3.5B (2-Stroke) Light 7.4 7 3  3F0641010M Moderate to Heavy 7.4 5.7 3 309641060M MFS4 / MFS5 / MFS6 (4-Stroke) Light 7.9 9 3 369W645181 Moderate 7.7 8 3 (5hp & 6hp) 3R1W645160 Heavy 7.7 7 3 (4hp) 3R1W645140 7.9 6 3 369W645120 M5B (2-Stroke) Light 7.9 9 3 369W645181 Moderate 7.7 8 3  3R1W645160 Heavy 7.7 7 3 3R1W645140 7.9 6 3 369W645120 M8 & M9.8 (2-Stroke) Light 8.5 9.5 3 3B2W645180 8.5 9 3 (short shaft) 3B2W645171 Moderate 8.5 8 3 (long shaft) 3B2W645150 8.9 7 3 3B2W645140 Heavy 8.7 7 4 (high thrust) 3B2W645120 8.5 6.5 3 3B2W645130 8 6 3 3B2W645126 8 5 3 3B2W645125 8.7 5 4 (high thrust) 3B2W645110 MFS8 & MFS9.8 (4-Stroke) Light 8.5 9.5 3 3B2W645180 8.5 9 3 (9.8hp short shaft) 3B2W645171 Moderate 8.5 8 3 (8hp ALL 9.8hp long/ultra-long shaft) 3B2W645150 8.9 7 3 3B2W645140 Heavy 8.7 7 4 (high thrust) 3B2W645120 8.5 6.5 3 3B2W645130 8 6 3 3B2W645126 8 5 3 3B2W645125 8.7 5 4 (high thrust) 3B2W645110 M9.9 & M15 (2-Stroke) Light 9.2 9.8 3 362W641080 9.2 9.1 3 362W641010 Moderate 9.2 8.8 3 (short shaft) 362W641020 9.2 7.8 3 (long shaft) 362W641030 Heavy 9.2 6.9 3 362W641050 9.2 6.1 3 362W641070 MFS9.9 / MFS15 / MFS18 / MFS20 (4-Stroke) Light 9.2 9.8 3 (15/18/20 short shaft) 362W641080 9.2 9.1 3 (9.9 short 15/18/20 long shaft) 362W641010 Moderate 9.2 8.8 3 (9.9 long shaft) 362W641020 9.2 7.8 3 362W641030 Heavy 9.2 6.9 3 362W641050 9.2 6.1 3 362W641070 M18 (2-Stroke) Light 9.2 9.8 3 362W641080 9.2 9.1 3 (short shaft) 362W641010 Moderate 9.2 8.8 3 (long shaft) 362W641020 9.2 7.8 3 362W641030 Heavy 9.2 6.9 3 362W641050 9.2 6.1 3 362W641070 M25 & M30 (2-Stroke) Light 9.9 14.2 3 346W641055 9.6 13 3 (short shaft) 3R0W645270 Moderate 9.8 12 3 3R0W645250 9.8 11 3 (long shaft) 3R0W645230 9.7 10 3 3R0W645210 Heavy 9.9 9.0 3 3R0645180M 10.2 8.3 3 346W641065 MFS25 & MFS30 (4-Stroke) Light 9.9 14.2 3 346W641055 9.6 13 3 3R0W645270 Moderate 9.8 12 3 3R0W645250 9.8 11 3 3R0W645230 9.7 10 3 3R0W645210 Heavy 9.7 9 3 3R0645180M 10.2 8.3 3 346W641065 M40C (2-cylinder) Light 11 15 3 3T5645320M 11.1 14 3 3T5645290M 11.1 13 3 3T5645270M Moderate 11.4 12 3 3T5645250M 11.6 11 3 3T5645230M 10.8 9.9 3 361W641090 Heavy 11.2 8.7 3 348W641070 11.4 7.1 4 348641080M M40D & M50D (3-cylinder) MD40 & MD50 (TLDI) Light 11 15 3 3T5645320M 11.1 14 3 3T5645290M Moderate 11.1 13 3 3T5645270M 11.4 12 3 3T5645250M Heavy 11.6 11 3 3T5645230M 12.1 9 3 3T5645180M 11.2 8.7 3 348W641070 11.4 7.1 4 348641080M M70A & M70B (2-Stroke) Light 10.9 17.6 3 353641090M 10.7 16.4 3 353641080M 11 15 3 353641070M Moderate 11.4 14 3 353641060M 11.5 13 3 353641050M 11.6 12 3 353641040M Heavy 11.5 11 3 353641030M 11.5 10 3 353641020M 12 9 3 353641010M M70C / M90 (2-Stroke) MD70 / NSD90 (TLDI) Light 12.75 21 3 3N4W645451 13 19 3 3N4W645411 13.25 17 3 3N4W645361 Moderate 13.25 16 3 3N4W645341 13.75 15 3 3N4W645321 Heavy 14 13 3 3N4W645271 14 11 3 3N4W645231 M115 & M140 (2-Stroke) Light 12.75 21 3 3N4W645451 13 19 3 3N4W645411 13.25 17 3 3N4W645361 Moderate 13.25 16 3 3N4W645341 13.75 15 3 3N4W645321 Heavy 14 13 3 3N4W645271 14 11 3 3N4W645231 MD115 (TLDI) Light 12.75 21 3 3T1W645450 13 19 3 3T1W645410 13.25 17 3 3T1W645360 Moderate 13.25 16 3 3T1W645340 13.75 15 3 3T1W645320 Heavy 14 13 3 3T1W645270 14 11 3 3T1W645230 The selection of the correct propeller will allow the engine to obtain it's full RPM as well as the designated horsepower. Engine horsepower is very closely related to the RPM that the outboard can obtain. In other words, if the outboard can not reach its specified RPM, it cannot reach its specified horsepower. We hope that this selection chart helps you in making the right decision when choosing a propeller for your Tohatsu outboard. STAINLESS STEEL PROPS Models Dia. Pitch Blades Part # 25/30 (2-Str & 4-Str) 10 9 4 NM889110109 10 10 4 NM889110110 10 8 3 NM889010108 10 9 3 NM889010109 10.125 10 3 NM889210100 10.125 11 3 NM889210110 10.125 12 3 NM889210120 10.125 13 3 NM889210130 40 - 50 (all models) 10.5 11 3 NM889410110 10.5 12 3 NM889410120 10.5 13 3 NM889410130 10.5 14 3 NM889410140 10.5 15 3 NM889410150 10.5 17 3 NM889410170 60A/70A/70B 11.75 15 3 NM889510150 11.75 17 3 NM889510170 60C/70C/90~140 (2-Str & TLDI) 13.25 14 3 NM889610140 13.25 15 3 NM889610150 13.25 16 3 NM889610160 13.25 17 3 NM889610170 13.25 18 3 NM889610180 13.25 20 3 NM889610200 Propeller Hardware Kits These Hardware Kits include the thrust holder, washer, nut and split pin. PROPELLER HARDWARE KITS Part Number Applicable Models 3H6-87326-0 M4C/5B/MFS4/5/6A & A2 & B 3V1-87326-0 M8/9.8B/MFS8/9.8A & A2 & A3 3V9-87326-0 M9.9/15D2/18E2/MFS9.9/15/18B2 3R0-87326-0 M25C3/30A4/MFS25/30A & B 361-87326-0 M40C 3T5-87326-0 M40/50D2/MD40/50B For other hardware kits for models not listed, please contact your local dealer.